## Slide 1: MTP EEPROM updating via i2c Rev-1.3 11/15/2024

## Slide 2: MTP product/Configuration Data / code patch Update
IND87451 I2C Slave Interface can be used for ISP (In System Programming). This is a mean to update the Product / Configuration Data and / or Code Patch stored inside the MTP.
To perform the ISP, the I2C Master controller must follow the recommended ISP protocol described in this document.
There are two types files will be loaded to MTP
  Product/Configuration data : 1K bytes
  Code Patch data : 31K bytes
IND87451
I2C Master
controller
MTP
I2C Slave
I2C Bus
ISP
Product configuration
Code Patch

## Slide 3: EEPROM Configuration Data
IND87451
IND87451 I2C master Interface can be used for updating of EERPOM. This is a mean to update the Configuration Data stored inside the EEPROM. And it can also use external i2c master control to update EEPROM
There is only one type file will be loaded to EEPROM
  Configuration data : 128 bytes
EEPROM
I2C Master
controller
I2C Bus
configuration
External I2C Master
controller
configuration
I2C Bus
JUMPs{J1,J2} = {[1-2],[1-2]}
JUMPs{J1,J2} = {[2-3],[2-3]}

## Slide 4: Product / Configuration Data
Total 1024B, can be divided into 2 major blocks – Product and Configuration data:
  Product data: 3 Sections
    Section #1 - Tracking & Production: It contains the record related FAB production data
    Section #2 - DUSR: It contains the Product name, Serial Number, and HDCP keys
    Section #3 - Calibration: It records the data calibrated from FAB
  Configuration data: 1 Section (#4), contains 3 Records
    Config0 record: It contains HW configuration and RX capability settings
    DPCD/VSF record: It contains Vendor Specific DPCD settings
    LVDS record: It contains LVDSTX configuration settings
And The 2.Configuration data will be stored in both MTP and EEPROM, while the 1.Product data will only be stored in MTP.
1
2

## Slide 5: code patch
The main purpose of Code Patch is to modify the incorrect programming in IROM.
The maximum size is 31KB on the top of MTP memory.
IROM currently has no code that needs to be modified, so no code patch data is generated yet.

## Slide 6: MTP Updating via I2C over DDC2BI with GPROBE command

## Slide 7: Gprobe commands and ddc2bi protocol
The GProbe commands used for ISP has the DDC2Bi3 wrapper. This makes the ISP messages compliant with the DDC2Bi protocol.
The DDC2Bi3 wrapper for ISP through the I2C Interface has the same message structure as the standard DDC2Bi3 used over the HDMI DDC interface.
  Consists of following message fields: DDC Destination, DDC Source, Length, VCP Prefix, Message and Checksum
The VCP prefix consists of two parts:
  VCP command code 0xC2: This particular code is undefined in the official DDC2Bi standard and is available for custom commands. Indie’s DDC2Bi3 wrapper uses the VCP command code 0xC2 and further expands it into the command page with the sub-commands specified in the remainder of the message.
  The command page: This is made up of two bytes following the VCP command code 0xC2. Indie reserves the command page 0x0000 for its own commands. Indie can assign individual command pages to its customers upon request, if customers wish to implement their own command sets for specific applications.

## Slide 8: DDC2Bi3 wrapper for ISP through the I2C Interface
Name | Length | Value | Comment
DDC Destination | 1 | 0x6E | 
DDC Source | 1 | 0x51 | Please note that length of VCP Prefix + Message can’t exceed 127
Length | 1 | 0x80 ¦ Length of VCP prefix + Message | 
VCP Prefix | 3 | 0xC2 0x00 0x00 | 
Message | variable |  | 
Checksum | 1 | XOR of all previous bytes | Byte chksum = 0 For(i=0;i<buffersz;i++) chksum ^= buf[i];

## Slide 9: Gprobe command loads 1KB Product / Configuration DATA into Sirius
S
0x37
Dst
0x51
Src
0x85
Length
0xC2 0x00 0x00
VCP Prefix
0x03 0x10
Message
0x6B
Chksum
0x00 0x01 0x30 0x00
Address = 0x13000
0x00 0x00 0x04 0x00
Count = 0x400
Payload, Size is 1024B
0x00 0x00 0x17 0xC2
CRC16 = 0x17C2
P
DDC2BI Header
Address (0x13000~0x133FF for Product/Configuration)
Count (Maximum: 0x400=1KB per message)
Message
CRC16
GProbe
MTPWrite
Command
CMD1
First command (0x10) writes Product/Configuration data (1KB) MTP SRAM in Sirius, noted as “CMD1”
GProbe Command
0x10 = MTPWrite

## Slide 10: Gprobe command loads 1KB Product/Configuration DATA into Sirius (conti.)
S
0x37
Dst
0x51
Src
0x85
Length
0xC2 0x00 0x00
VCP Prefix
0x03 0x07
Message
0x7C
Chksum
0x00 0x01 0xFF
P
DDC2BI Header
Message for executing
CMD2
Second command (0x07) that updates Product/Configuration Data from MTP SRAM to MTP (in Sector 3), noted as “CMD2”
GProbe Command
0x07 = MTPUpdate
Executes CMD1 and CMD2 to complete the Product/Configuration Data update into MTP
CMD2
CMD1

## Slide 11: Gprobe command loads 31KB code patch DATA into Sirius
S
0x37
Dst
0x51
Src
0x85
Length
0xC2 0x00 0x00
VCP Prefix
0x03 0x10
Message
0x6B
Chksum
0x00 0x30 (0x00 0x00 + 0x400 * X)
Address = 0x300000
0x00 0x00 0x04 0x00
Count = 0x400
Payload, Size is 1024B
0x00 0x00 0x17 0xC2
CRC16 = 0x17C2
P
DDC2BI Header
Address (0x300000~0x307FFF for Code Patch)
Count (Maximum: 0x400=1KB per message)
Message
CRC16
GProbe
MTPWrite
Command
CMD3-1
First command (0x10) that writes Code Patch data (max 31KB) into MTP SRAM in Sirius, noted as “CMD3-X”.
As payload size is up to 1024B for each command and size of the Code Patch is varied (between 0~31KB), will need to divide into multiple MTPWrite commands to complete. Where X = Code Patch size / 1024, and the size of the last payload, X+1, = Code Patch size % 1024 (if non-zero)
GProbe Command
0x10 = MTPWrite
CMD3-2
CMD3-3
…..
CMD3-X
CMD3-(X+1)

## Slide 12: Gprobe command loads 31KB code patch DATA into Sirius (conti.)
S
0x37
Dst
0x51
Src
0x85
Length
0xC2 0x00 0x00
VCP Prefix
0x03 0x07
Message
0x7C
Chksum
0x00 0x01 0xFF
P
DDC2BI Header
Message for executing
CMD4
Second command (0x07) that updates Code Patch Data from MTP SRAM to MTP Sector 0-3, noted as “CMD4”
GProbe Command
0x07 = MTPUpdate
Executes the CMD3-1~CMD3-(X+1) and CMD4 to complete the Code Patch Data update into MTP
CMD3-2
CMD3-1
CMD3-X
CMD3-3
…..
CMD3-(X+1)
CMD4

## Slide 13: Binary files convert to the sequence of I2C controller with Python

## Slide 14: Original binary FILES
indie will prepare Product/Configuration(1KB) and Code Patch(XKB, max 31KB) binary files for Tesla and ATE to do MTP updating
Product data
Code Patch
Configuration data
356B bin
128B bin
XKB bin
ATE
Tesla

## Slide 15: Python script to generate files for I2C update sequence(MTP/EEPROM)
Convert Product/Configuration Data or Code Patch binary to files for ISP
  Install Python (v3.12.6)
  Execute Python script :
    Python modify_binary_file.py [Type] [InputBIN] [OutputBIN] [OutputXML][Slaveaddr]
    Type:
      codepatch: Input binary contains Code Patch
      mtpfull: Input binary contains all Product related records (Tracking & Production / DUSR / Calibration Data in Sections 1-3) and Configuration Data related records (CONFIG0 / DPCD_VSF / LVDS_CONFIG in Section 4)
      mtpproduct: Input binary contains only Product related records
      mtpconfig: Input binary contains only Configuration Data related records
      eeprom: Input binary contains only Configuration Data related records for EPROM updates
    InputBIN: Original Product / Configuration Data or Code Patch binary array file
    OutputBIN: Converted binary array file for I2C update sequence. It can be used in script(s) or batch(es) for customer’s I2C master device. It is currently not used, but for possible usage in the future.
    OutputXML: To run in Total Phase Control Center Batch Mode with Aardvark I2C/SPI Host Adapter
    Slaveaddr To input EEPROM’s slave address(default value is 0x54)
NOTE: Will not support the individual Configuration Data record update to MTP. All the 3 Configuration Data records (CONFIG0 / DPCD_VSF / LVDS_CONFIG) shall be combined in one binary and programmed together to avoid number of MTP programming times and risks to accidently corrupt the Product related records.

## Slide 16: Example of sequence to update 1kb DATA to MTP – 1 (case: Product + Configuration DATA)
Run Python script from Windows Command Prompt to generated converted files:
> Python modify_binary_file.py mtpfull MTP_DATA_1K.bin MTP_DATA_1K_Converted.bin mtp_batch.xml
After executing python
mtp_batch.xml

## Slide 17: Example of sequence to update 1kb DATA to MTP – 1-1 (case: Product + Configuration DATA)
After executing python
DDC2BI Header
MTP data
MTP_DATA_1K.bin
MTP_DATA_1K_Converted.bin

## Slide 18: Example of sequence to update 1kb DATA to MTP – 1-2 (case: product DATA only)
Run Python script from Windows Command Prompt to generated converted files separately:
> Python modify_binary_file.py mtpproduct MTP_DATA_1K.bin MTP_DATA_1K_ProductConverted.bin mtp_Product_batch.xml
After executing python
mtp_Product_batch.xml

## Slide 19: Example of sequence to update 1kb DATA to MTP – 1-3 (case: Product DATA only)
After executing python
DDC2BI Header
MTP product data
CRC16 for DDC2Bi
MTP_DATA_1K.bin
MTP_DATA_1K_ProductConverted.bin

## Slide 20: Example of sequence to update 1kb DATA to MTP – 1-4 (case: Product DATA only)
After executing python
MTP_DATA_1K.bin
mtpproduct.bin

## Slide 21: Example of sequence to update 1kb DATA to MTP – 1-5(case: Configuration DATA only)
Run Python script from Windows Command Prompt to generated converted files separately:
> Python modify_binary_file.py mtpconfig MTP_DATA_1K.bin MTP_DATA_1K_ConfigConverted.bin mtp_Config_batch.xml
After executing python
mtp_Config_batch.xml

## Slide 22: Example of sequence to update 1kb DATA to MTP – 1-6 (case: Configuration DATA only)
After executing python
MTP configuration data
MTP_DATA_1K.bin
mtpconfig.bin
DDC2BI Header
MTP configuration data
CRC16 for DDC2Bi
MTP_DATA_1K_ConfigConverted.bin

## Slide 23: Example of sequence to update 1kb DATA to MTP – 2
If use Aardvark to update, load the mtp_batch.xml file from Total Phase Control Center  Adapter  Batch Mode. Then hit “Execute” button after loaded.
NOTE: This step only writes the binary into Sirius’s SRAM memory for MTP. Yet updating to MTP.

## Slide 24: Example of sequence to update 1kb DATA to MTP – 3
After writing to Sirius internal memory is done, load the MTPDATA_update_execute.xml file from Total Phase Control Center  Adapter  Batch Mode. Then hit “Execute” button to start updating to MTP (from SRAM).

## Slide 25: EEPROM Updating via I2C

## Slide 26: EEPROM hardware feature
The EEPROM has three hardware detection PINs, A0, A1, and A2 in the picture below. They can decide the i2c slave address of EEPROM
PINs{A2,A1,A0} | i2c slave address(7-bit)
{0,0,1} | 0x51
{0,1,0} | 0x52
{0,1,1} | 0x53
{1,0,0} | 0x54
{1,0,1} | 0x55
{1,1,0} | 0x56
{1,1,1} | 0x57
The EEPROM has a data transfer limitation: a 1ms delay must be added after every 8-byte(as payload size) of I2C transfer

## Slide 27: I2c sequence loads 128B configuration DATA into EEPROM
I2C protocol write:
S
Slave address(7bit)
+0 for write bit
Reg. address
(Byte *)Data
P
I2C Write
Command
For example:
S
0xA8
0x00
0xAA 0x55 0x00 0x30 0x00 …
P
PINs{A2,A1,A0} = {1,0,0}  slave address = 0x54  write command : 0xA8
S
Slave address(7bit)
+0 for writing bit
Reg. address
(Byte *) Data
P
I2C Read
Command
Slave address(7bit)
+1 for reading bit
S
0xA8
0x00
0xAA 0x55 0x00 0x30 0x00 …
P
PINs{A2,A1,A0} = {1,0,0}  slave address = 0x54  read command : 0xA9
0xA9

## Slide 28: Example of sequence to update EERPOM via external i2c master (AADVARK)
Continue Configuration DATA update on page-21. Run Python script from Windows Command Prompt to generate aadvark batch file:
  Python modify_binary_file.py eeprom MTP_DATA_1K.bin EEP_DATA_1K_ConfigConverted.bin eep_Config_batch.xml 0x54
MTP_DATA_1K.bin
The parameter is EEPROM’s slave address
EEP_DATA_1K_ConfigConverted.bin
eep_Config_batch.xml

## Slide 29: Example of sequence to update EERPOM via SIRIUS i2c master (Appstest)
Run Python script from Windows Command Prompt to generate AppsTest batch file:
Python modify_binary_file.py eeprom MTP_DATA_1K.bin EEP_DATA_1K_ConfigConverted.bin eep_Config.batch
Note: This example is for indie’s Sirius EV board that has UART enabled to execute AppsTest batch from indie’s Windows GProbe tool.
eepconfig.bin
APPSTEST_EEPROM_Updata_script.batch

## Slide 30: EEPROM Updating via HostInterface

## Slide 31: The Virtual registers(VR) with eeprom
Offset/data register
Update register
0x06 |  | 
Bit | Bit name | Function
7:0 | CONFIG0_PL_OFF | Payload Offset for CONFIG0 Record
15:8 | CONFIG0_PL_BYTE | 8bit data for offset CONFIG0 Payload
0x08 |  | 
Bit | Bit name | Function
7:0 | DPCD_VSF_PL_OFF | Payload Offset for DPCD VSF Record
15:8 | DPCD_VSF_BYTE | 8bit data for offset DPCD VSF Payload
0x0A |  | 
Bit | Bit name | Function
7:0 | LVDS_CONFIG_PL_OFF | Payload Offset for LVDS CONFIG Record
15:8 | LVDS_CONFIG_PL_BYTE | 8bit data for offset LVDS CONFIG Payload
0x0B |  | 
Bit | Bit name | Function
0 | LVDS_CONFIG_UPDATE_DONE | Sirius will Calculate CRC, create Record and program EEPROM locations for this record when this bit is set.
1 | LVDS_CONFIG_UPDATE_EEPROM_DONE | EEPROM update is done with HI interrupt. Host can restart Sirius and use the Configuration Data from EEPROM to initialize the system.
0x07 |  | 
Bit | Bit name | Function
0 | CONFIG0_UPDATE_DONE | Sirius will Calculate CRC, create Record and program EEPROM locations for this record when this bit is set.
1 | CONFIG0_UPDATE_EEPROM_DONE | EEPROM update is done with HI interrupt. Host can restart Sirius and use the Configuration Data from EEPROM to initialize the system.
0x09 |  | 
Bit | Bit name | Function
0 | DPCD_VSF_UPDATE_DONE | Sirius will Calculate CRC, create Record and program EEPROM locations for this record when this bit is set.
1 | DPCD_VSF_UPDATE_EEPROM_DONE | EEPROM update is done with HI interrupt. Host can restart Sirius and use the Configuration Data from EEPROM to initialize the system.

## Slide 32: Update steps – for an example : change of LVDS config byte1 to be 0x33
P
1. Use VR 0x0A to update the value of LVDS config BYTE1
2. Use VR 0x0B to perform calculation of CRC16 and write to EEPROM
S
0xE0
0x0A 0x01 0x33
VR address 0x0A
Payload byte 0x33
Payload offset 0x01
HostInterfase slave address 0xE0 for writing, 0xE1 for reading --> 7bit : 0x70
P
S
0xE0
0x0B 0x01 0x00
VR address 0x0B
LVDS_CONFIG_UPDATE_DONE = 1
HostInterfase slave address 0xE0 for writing, 0xE1 for reading --> 7bit : 0x70
CMD1
CMD2

## Slide 33: Update steps – for an example : change of LVDS config byte1 to be 0x33
1. Check the status of VR 0x0B -- If LVDS_CONFIG_UPDATE_EEPROM_DONE is set to 1, it means that the new value and the calculated new CRC16 are updated to the EEPROM.
S
0xE0
0x0B
VR address 0x0B
0x02 0x00
P
0xE1
HostInterfase slave address 0xE0 for writing, 0xE1 for reading --> 7bit : 0x70
LVDS_CONFIG_UPDATE_EEPROM_DONE=1
CMD3
CMD1
CMD2
VR 0x0B =0x0000
VR 0x0B =0x0002

## Slide 34: Appendix
Calculation of CRC 16

## Slide 35: Calculation of CRC 16(Python code)
def calculate_crc16(Buf: bytes, W_len: int) -> int:
Accum = 0x1021
PolDiv = 0x1021
for j in range(W_len):
DataIn = Buf[j]
for _ in range(8):
flag = DataIn ^ (Accum >> 8)
Accum <<= 1
if flag & 0x80:
Accum ^= PolDiv
DataIn <<= 1
Accum &= 0xFFFF
return Accum